## Slide 1: CS 488 Computer Network and the Internt
Lecture 9-2: Router design and IP match
Prepared by: Jun Yuan
Credits: Srinivas Narayana

## Slide 2: Network
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
X.25
ATM
HTTPS
The main function of the network layer is to
move packets from one endpoint to another.
The network will make its best effort to deliver packets
but doesn’t guarantee anything.

## Slide 3: This lecture is about routers
Access routers
Core router
Data center top-of-rack switch

## Slide 4: What’s inside a router?

## Slide 5: Router architecture overview
high-speed
switching
fabric
route
processor
router input ports
router output ports
Control plane
Data plane
Review: Forwarding function: move packets from one input port to another.
Review: assuming distributed routing, routing function: decide which ports packets need to exit

## Slide 6: Different and evolving designs
There are different kinds of routers, with their own designs
  Access routers (e.g., home WiFi), chassis/core routers, top-of-rack switches
Router designs have also evolved significantly over time
For simplicity and concreteness, we will learn about one high-speed router design from the early 2000s.
Called the MGR (multi-gigabit router). It could support an aggregate rate of 50 Gbit/s (1 G = 109)
  Today’s single-chip routers can support aggregate rates of ~10 Tbit/s (1 T = 1012)

## Slide 7: Input port functions
Line termination: receives physical (analog) signals and turns them into digital signals.
Speed of data on a single network interface termed line speed or line rate (e.g., 100 Mbit/s)
Link layer: performs medium access control functions (e.g., Ethernet): more on this much later.
Line
Term
Link
Layer
/ MAC
(receive)
Route
lookup
switching
fabric
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Per-output
Queues

## Slide 8: Input port functions
Route lookup: high-speed lookup of which output port the packet is destined to
Goal: must complete this processing at the line rate
Queueing: packets may wait in per-output-port queues if packets are arriving too fast for the switching fabric to send them to the output port
Line
Term
Link
Layer
/ MAC
(receive)
Route
lookup
switching
fabric
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Per-output
Queues

## Slide 9: Route lookups
Packet forwarding in the Internet is based on the destination IP address on the packet.
Example: if dst IP on packet is 65.45.145.34, it matches the forwarding table prefix 65.0.0.0/8.
The packet is forwarded out port 3.
Line
Term
Link
Layer
Route
lookup
Per-output
Queues
Outgoing Port
Dst-network
Port
Forwarding Table
Route Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
Parse
Transport
Network
Link layer
Extract destination IP address

## Slide 10: Route lookups
Number of entries in the forwarding table matters.
Fitting into router memory
Designing hardware and software for fast lookups
Line
Term
Link
Layer
Route
lookup
Per-output
Queues
Outgoing Port
Dst-network
Port
Forwarding Table
Route Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
Parse
Transport
Network
Link layer
Extract destination IP address

## Slide 11: Route lookups
Recall: IP addresses can be aggregated based on shared prefixes.
The number of table entries in a router is proportional to the number of prefixes, NOT the number of endpoints.
Today: ~ 1 million prefixes.
Line
Term
Link
Layer
Route
lookup
Per-output
Queues
Outgoing Port
Dst-network
Port
Forwarding Table
Route Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
Parse
Transport
Network
Link layer
Extract destination IP address

## Slide 12: Route lookups
Destination-IP-based forwarding has consequences.
Forwarding behavior is independent of the source: legitimate source vs. malicious attack traffic
Forwarding behavior is independent of the application: web traffic vs. file download vs. video
IP-based packet processing is “baked into” router hardware: evolving the IP protocol faces tall deployment hurdles
Line
Term
Link
Layer
Route
lookup
Per-output
Queues
Outgoing Port
Dst-network
Port
Forwarding Table
Route Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
Parse
Transport
Network
Link layer
Extract destination IP address

## Slide 13: Types of fabrics
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Input port writes packets into shared memory.
Output port reads the packet when output link ready to transmit.
Single shared channel to move data from input to output port.
Easy to build buses; technology is quite mature.
Each input port has a physical data path to every output port.
Switch at the cross-over points turns on to connect pairs of ports.

## Slide 14: Types of fabrics
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Modern high-speed routers use highly optimized shared-memory-based interconnects.
Crossbars can get expensive as the number of ports grows (N2 connections for N ports)
MGR uses a crossbar and schedules (in,out) port pairs.

## Slide 15: Fabrics
High-speed switching fabrics designed to be nonblocking:
  If an output port is “available”, an input port can always transmit to it without being blocked by the switching fabric itself
Crossbars are nonblocking by design
Shared memory can be designed to be nonblocking if memory is optimized to be fast enough for the access pattern
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port

## Slide 16: Fabrics
With a nonblocking fabric, queues aren’t formed due to the switching fabric.
  i.e., there are no queues due to inefficiencies at the input port or the switching fabric
Queues only form due to contention for the output port
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port

## Slide 17: Fabrics
With a nonblocking fabric, queues aren’t formed due to the switching fabric.
  i.e., there are no queues due to inefficiencies at the input port or the switching fabric
Queues only form due to contention for the output port
Typically, these (per-output-port) queues form on the output side
  But queues can also form on the input side if the fabric can’t even move packets to the output port’s buffer (ie: if output-side buffer filled up)
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port

## Slide 18: Output port functions
Components in reverse order of those in the input port
This is where most routers have the bulk of their packet buffers
  Recall our discussions regarding router buffer sizes in the transport layer
MGR uses per-port output buffers, but modern routers have shared memory buffers
  More efficient use of memory under varying demands
Line
Termination
Link
Layer
/ MAC
(transmit)
Queues
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Switching
fabric
To output link

## Slide 19: Output port functions
Two important policy decisions
Scheduling: which among the waiting packets gets to be transmitted out the link?
  Ex: First-In-First-Out (FIFO)
Buffer management: which among the packets arriving from the fabric get space in the packet buffer?
  Ex: Tail drop: later packets dropped first
Line
Termination
Link
Layer
/ MAC
(transmit)
Queues
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Switching
fabric
To output link

## Slide 20: Control (plane) processor
A general-purpose processor that “programs” the data plane:
  Forwarding table
  Scheduling and buffer management policy
Implements the routing algorithm by processing routing protocol messages
  Mechanism by which routers collectively solve the Internet routing problem
  More on this soon.
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Control Processor

## Slide 21
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header, i.e, destination IP address
3
Data plane
per-packet processing
(~ tens of nanoseconds)
Control plane
Traditional distributed routing: per route-change processing
(~ a few tens of seconds)
Router design: the bigger picture

## Slide 23: Longest Prefix Matching

## Slide 24: Review: Route lookup
Table lookup matches a packet against an IP prefix
  Ex: 65.12.45.2 matches 65.0.0.0/8
Prefixes are allocated to organizations by Internet registries
But organizations can reallocate a subset of their IP address allocation to other orgs
Outgoing Port
Dst-network
Port
Forwarding Table
Route Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
Parse
Transport
Network
Link layer
Extract destination IP address

## Slide 25: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
… | …
200.23.16.0/20 | 7 (towards A)
There is an announcement mechanism (BGP) by which ISP A can inform the rest of the Internet about the prefixes it owns.
It is enough to announce a coarse-grained prefix 200.23.16.0/20 rather than 8 separate sub-prefixes.
Send me pkts for
200.23.16.0/20

## Slide 26: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
… | …
200.23.16.0/20 | 7 (towards A)
Now suppose one of these organizations chooses to connect to a different ISP for its Internet service.
It is possible for this organization to retain its assigned IP block.
Send me pkts for
200.23.16.0/20

## Slide 27: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
… | …
200.23.16.0/20 | 7 (towards A)
200.23.18.0/23
Organization 2
ISP B
Announce 200.23.18.0/23
(besides other IP blocks)
Send me pkts for
200.23.16.0/20

## Slide 28: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
200.23.18.0/23 | 4 (towards B)
200.23.16.0/20 | 7 (towards A)
200.23.18.0/23
Organization 2
ISP B
Announce 200.23.18.0/23
(besides other IP blocks)
Send me pkts for
200.23.16.0/20

## Slide 29: A closer look at the forwarding table
200.23.18.0/23 is inside 200.23.16.0/20
A packet with destination IP address 200.23.18.xx is in both prefixes
  i.e., both entries match
Q: How should the router choose to forward the packet?
  Clearly, towards ISP B
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
200.23.18.0/23 | 4 (towards B)
200.23.16.0/20 | 7 (towards A)
200.23.16.0/20

## Slide 30: Longest Prefix Matching (LPM)
Use the longest matching prefix, i.e., the most specific route, among all prefixes that match the packet.
Policy borne out of the Internet’s IP allocation model: prefixes and sub-prefixes are handed out
Internet routers use longest prefix matching.
  Very interesting algorithmic problems
  Challenges in designing efficient software and hardware
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
200.23.18.0/23 | 4 (towards B)
200.23.16.0/20 | 7 (towards A)
200.23.16.0/20