## Slide 1: CS 488 Computer Networks and the Internet
Lecture 11-2: Inter-domain routing
Prepared by: Jun Yuan
Credits: Srinivas Narayana

## Slide 2: Network
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
X.25
ATM
HTTPS
The main function of the network layer is to
move packets from one endpoint to another.

## Slide 3: Routing so far
Routers know the existence of all other routers
  It’s safe to exchange neighborhood information
All link metrics are known
It is feasible to exchange info at scale
  LS: Link state advertisement flooding throughout the network
  DV: Distance vectors to all other routers is small enough to exchange
It is difficult to scale this approach to the Internet
Distance vector protocols
Routing protocols
Link state
protocols

## Slide 4: The Internet is not a “flat” network

## Slide 5: The Internet is a network of networks
Pace
AT&T
Sprint

## Slide 6: Constraints of the Internet
Administrative autonomy
  The Internet is not owned by any one organization
  Rather, it is a network of organizations interconnected with each other
  The network graph, the link metrics, the IDs and locations of routers are not public information
Scale
  It is unscalable to flood LSAs all over the Internet
  Sending a vector containing distances to all other Internet routers will swamp network links

## Slide 7: The Internet’s approach
Split the network into separately administered autonomous systems (AS’es)
  Pace is an autonomous system
  So are AT&T, Verizon, and Comcast
Use different approaches for routing within AS’es and routing across AS’es
Distributing the administration helps scale to larger networks
  Ex: think about Government: federal  state  city  boro  …

## Slide 8: Intra-domain routing: Routing within AS’es
The approaches we’ve studied so far are applicable within an AS!
It is safe for routers within an AS to know the existence of other routers and all link metrics within the same organization
It is indeed feasible to use link state flooding or exchange distance vectors to all other routers
  Such approaches won’t scale to Internet size
Different AS’es can use different intra-domain routing protocols: e.g., OSPF (LS), RIP (DV)
Routers within an AS must use the same protocol
Distance vector protocols
Routing protocols
Link state
protocols

## Slide 9: Inter-domain routing: Routing across AS’es
Routing information is exchanged at a coarser granularity
  Don’t announce per-router info; instead, announce per AS info
  (The assignment of IP prefixes to AS’es is public information)
  Path announced per destination, not for all destinations
Link metrics are not exchanged (not public info)
  Instead, the entire path available to the destination is exchanged
Only the routers at the border of two networks need to speak the inter-domain routing protocol: border/gateway routers
However, all AS’es need to speak the same inter-domain routing protocol
  Next, we’ll study this protocol: Border Gateway Protocol (BGP)

## Slide 10: The Internet is a network of networks
Verizon
Pace
AT&T
Sprint
Intra-domain
Protocol 1
Intra-domain
Protocol 2
The same interdomain routing protocol

## Slide 11
Routing protocols
Link state protocols
e.g., OSPF, IS-IS
Distance vector protocols
e.g., RIP, IGRP
Intra-domain protocols
same protocol within an AS
different algorithms across ASes
(semi)global view of the org’s network
Sometimes called interior gateway protocols (IGP)
Path vector protocols
BGP
Inter-domain protocol
common across AS’es
each AS knows little about the others

## Slide 13: Border Gateway Protocol

## Slide 14
Routing protocols
Link state protocols
e.g., OSPF, IS-IS
Distance vector protocols
e.g., RIP, IGRP
Intra-domain protocols
Path vector protocols
BGP
Inter-domain protocol
The glue that holds the Internet together.

## Slide 15: Border Gateway Protocol
The de facto inter-domain routing protocol
Two parts to BGP:
  eBGP: each AS can obtain reachability information from neighboring AS’es
  iBGP: each AS propagates reachability information about external AS’es to all AS-internal routers.
Q1: What computation occurs at each router?
Q2: What information is exchanged?

## Slide 16: Q2. BGP announcements
eBGP allows a network to advertise its existence to the rest of the Internet using eBGP announcements
Announcements occur over a BGP session
  Semi-permanent TCP connection between gateway routers
Announcements contain AS-level paths to IP prefixes
  BGP is a path vector protocol
1b
1d
1c
1a
2b
2d
2c
2a
AS 1
AS 2

## Slide 17: Q2. BGP announcements
Suppose AS2’s gateway router 2a announces path AS2,X to AS1’s gateway router 1c
AS2 promises that it will forward datagrams towards X
Announcements contain the IP prefix destination as well as attributes
Two important attributes: AS-path (AS2,X), Next-Hop
1b
1d
1c
1a
2b
2d
2c
2a
AS 1
AS 2
eBGP announcement:
AS2, X
X

## Slide 18: Q2. BGP announcements: Next Hop
Next hop conceptually denotes the next hop router that must be used to reach a specific destination.
  However, the meaning of this attribute is context-dependent
In an eBGP announcement, next hop denotes the router in the next AS which sent the announcement
Next Hop of the eBGP announcement reaching 1c is 2a
1b
1d
1c
1a
2b
2d
2c
2a
AS 1
AS 2
eBGP announcement:
AS2, X
X

## Slide 19: Q2. BGP announcements: Next Hop
Suppose router 1c accepts the path (more on this soon)
Router 1c will propagate the announcement inside the AS using iBGP
The next hop of the iBGP announcement from 1c to 1a is set to router 1c
  In particular, the next hop is an AS1 internal address
1b
1d
1c
1a
2b
2d
2c
2a
AS 1
AS 2
eBGP announcement:
AS2, X
X

## Slide 20: Q1. What is computed?
Upon receiving an announcement, a BGP router chooses routes to other networks based on policy considerations
This approach is very different from the link-metrics-based approaches we’ve seen earlier
Export policy determines whether a path is announced
Import policy determines whether a path is accepted
1b
1d
1c
1a
2b
2d
2c
2a
X
eBGP announcement:
AS2, X
AS 1
AS 2

## Slide 21: Policies in BGP

## Slide 22: Policy arises from business relationships
Customer-provider relationships:
  E.g., Pace is a customer of AT&T
Peer-peer relationships:
  E.g., Verizon is a peer of AT&T
Business relationships depend on where connectivity occurs
  “Where”, also called a “point of presence” (PoP)
  e.g., customers at one PoP but peers at another
  Internet-eXchange Points (IXPs) are large PoPs where ISPs come together to connect with each other (often for free)
Sometimes, even when there is no direct connectivity
  “e.g., inteliquent (zoom/webex) traffic should not be charged”

## Slide 23: BGP Export Policy
A,B,C are provider networks
X,W,Y are customers (of provider networks)
X is dual-homed: attached to two networks
policy to enforce: X does not want to route from B to C via X
  so X will not announce to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)

## Slide 24: BGP Export Policy
A announces path Aw to B and to C
B chooses not to announce BAw to C:
  B gets no “revenue” for routing CBAw, since none of C, A, w are B’s customers
C will route CAw (not using B) to get to w
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)

## Slide 25: BGP Import Policy
Suppose C announces path Cy to x
Further, y announces a direct path (“y”) to x
Then x might reject the path Cy towards y in favor of using the direct path (“y”) towards y: reduce costs by avoiding provider network
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP wants to minimize costs by avoiding routing through its providers when possible.

## Slide 26
Policies make BGP a complex protocol.
Policy considerations dominate performance considerations (e.g., no “link metrics” for AS paths).
BGP chooses to announce (export) only certain paths.
BGP chooses to accept (import) only certain paths.
A complex decision process prefers certain paths over others.

## Slide 27: Q1. BGP route selection process
When a router learns more than one acceptable route to a destination AS, it selects route based on:
  local preference value attribute (policy decision, set by network admin)
  shortest AS-PATH
  closest NEXT-HOP router
  Several additional criteria: You can read up on the full, complex, list of criteria, e.g., at https://www.cisco.com/c/en/us/support/docs/ip/border-gateway-protocol-bgp/13753-25.html

## Slide 28: Example of route selection
Suppose AS A and B are connected to each other both in North America (NA) and in Europe (EU)
A source in NA wants to reach a destination in EU
There are two paths available
  Assume same local preference
  Same AS path length
Closest next hop-router: choose path via B1 rather than B2
A1
B1
A2
B2
Src-NA
Dst-EU
AS B
AS A
NA
EU

## Slide 29: Example of route selection
Choosing closest next-hop results in early exit routing
  Try to exit the local AS as early as possible
  Also called hot potato routing
Reduces bandwidth use within the local AS
  … potentially at the expense of another AS
A1
B1
A2
B2
Src-NA
Dst-EU
AS B
AS A
NA
EU

## Slide 30: Summary of BGP
BGP is the protocol that enables communication across multiple autonomous systems in the Internet
Border routers exchange AS-level paths to prefixes via eBGP, propagate those prefixes to internal routers via iBGP
  Path vector protocol
BGP routers use a complex policy-based procedure to choose the final path and next hop for a given IP prefix destination
  Local pref, AS path length, closest next hop, and other criteria

## Slide 32: Forwarding to External Destinations

## Slide 33
Routing protocols
Link state protocols
e.g., OSPF, IS-IS
Distance vector protocols
e.g., RIP, IGRP
Path vector protocols
BGP
Border Gateway Protocol:
The glue that holds the Internet together.

## Slide 34: Review: BGP
Two parts to BGP:
eBGP announcements from external AS’es carry information about IP prefixes reachable through an AS
iBGP propagates announcements received from external AS’es to AS-internal routers
BGP announcements contain an IP prefix and attributes
This module: One of the attributes of the BGP announcement, Next Hop, is key to generating forwarding tables for all routers

## Slide 35: Forwarding to an external prefix

## Slide 36: Example scenario
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
Suppose a router in AS1 wants to forward a packet destined to external prefix X.
How is the forwarding table entry for X at 1d computed?
How is the forwarding table entry for X at 1c computed?

## Slide 37: eBGP and iBGP announcements
Based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS2 router 2c receives path announcement AS3,X (via eBGP) from AS3 router 3a
Based on AS2 policy, AS2 router 2a announces (via eBGP) path AS2, AS3, X to AS1 router 1c

## Slide 38: eBGP and iBGP announcements
AS1 gateway router 1c learns path AS2,AS3,X from 2a
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
Gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a (next hop 3a)
Based on policy, AS1 gateway router 1c chooses path AS3,X, and announces path within AS1 via iBGP (next hop 1c)

## Slide 39: Setting forwarding table entries
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS3,X
recall: 1a, 1b, 1d learn about dest X via iBGP from next-hop 1c: “path to X goes through 1c”
1d: intra-domain routing: to get to 1c, forward over outgoing local interface 1
NH
interface
…
…
1c
…
…
1
dest
Next-Hop
…
…
X
…
…
1c
1
2
3

## Slide 40: Setting forwarding table entries
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS3,X
recall: 1c learns about dest X via eBGP from next-hop 3a: “path to X goes through 3a”
1c: to get to link-local neighbor 3a, forward out interface 2
NH
interface
…
…
3a
…
…
2
dest
Next-Hop
…
…
X
…
…
3a
1
2
3

## Slide 41: Summary: Computing forwarding table
Intra- and inter-domain protocols collaborate to form the final forwarding table at each router
eBGP next hop is the external router that provided the announcement
iBGP next hop is the internal router that is used to reach the eBGP next hop