## Slide 1: CS 488 Computer Networks and the Internet
Lecture 8-1: Ordered Delivery
Prepared by: Jun Yuan
Credits: Srinivas Narayana

## Slide 2: Transport
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
X.25
ATM
HTTPS

## Slide 3: Modularity through layering
Link: best-effort local pkt delivery
Network: best-effort global pkt delivery
Transport: provide guarantees to apps
Apps: useful user-level functions
HTTP
FTP
TFTP
NV
TCP
UDP
IP
Ether
ATM
WiFi
…

## Slide 4: How do apps get perf guarantees?
The network core provides no guarantees on packet delivery
Transport software on the endpoint oversees implementing guarantees on top of a best-effort network
Three important kinds of guarantees
  Reliability
  Ordered delivery
  Resource sharing in the network core
Transmission Control Protocol (TCP)

## Slide 5: Reordering packets at the receiver side
Let’s suppose receiver gets packets 1, 2, and 4, but not 3 (dropped)
Suppose you’re trying to download a Word document containing a report
What would happen if transport at the receiver directly presents packets 1, 2, and 4 to the Word application?
Sender
Receiver
1
2
3
4
1
2
4
5

## Slide 6: Reordering at the receiver side
Reordering can happen for a few reasons:
  Drops
  Packets taking different paths through a network
Receiver needs a general strategy to ensure that data is presented to the application in the same order that the sender side pushed it
Receiver uses two mechanisms:
  Sequence numbers
  Receiver socket buffer
We’ve already seen the use of both of these for reliability
Sender
Receiver
1
2
3
4
1
2
4
5
3

## Slide 7: Interaction between apps and TCP
Sender deposits data in receiver socket buffer
An app with a TCP socket reads from the TCP receive socket buffer
  e.g., when you do data = sock.recv()
TCP receiver software only releases this data to the application if the data is in order relative to all other data already read by the application
This process is called TCP reassembly
application
process
TCP socket
receiver buffers
TCP
code
receiver protocol stack
from sender
recv()

## Slide 8: TCP Reassembly
1
2
1
2
4
1
2
4
3
Application can read up to here
Sender/Net writes here
Socket buffer memory on the receiver

## Slide 9: Sequence numbers in the app’s stream
TCP uses byte sequence numbers
Increasing sequence #s
…
…
packet
packet
packet
packet
packet
Data written by application over time
e.g., send() call
100
150
180
240
273
310

## Slide 10: Sequence numbers in the app’s stream
Packet boundaries aren’t important for TCP software
TCP is a stream-oriented protocol
(We use SOCK_STREAM when creating sockets)
Increasing sequence #s
…
…
packet
packet
packet
packet
packet
Data written by application over time
e.g., send() call
100
150
180
240
273
310

## Slide 11: Sequence numbers in the app’s stream
…
…
Data written by application over time
e.g., send() call
App does a recv()
1st recv()
2nd recv()
3rd recv()
4th recv()
A recv() call may return a part of a packet, a full packet, or multiple packets together.

## Slide 12: Implications of ordered delivery
Packets cannot be delivered to the application if there is an in-order packet missing from the receiver’s buffer
  The receiver can only buffer so much out-of-order data
  Subsequent out-of-order packets dropped (it doesn’t matter that those packets successfully arrive at the receiver from the sender over the network)
TCP application-level throughput will suffer if there is too much packet reordering in the network
  Data may reach the receiver
  But won’t be delivered to apps upon a recv()

## Slide 13: Summary of TCP ordered delivery
In-order delivery accomplished through socket buffer and TCP reassembly at receiver
TCP is a stream-oriented protocol, where the boundaries between packets aren’t important
Significant packet reordering reduces TCP application throughput

## Slide 15: Flow Control

## Slide 16: Review: app and socket buffer interaction
Sender deposits data in receiver socket buffer
An app with a TCP socket reads from the TCP receive socket buffer
  e.g., when you do data = sock.recv()
Buffers used for ordering & reliability
Ordering: only release data to app when data in order with everything else app has read previously
Reliability: avoid wasteful sender retransmissions using selective repeat
application
process
TCP socket
receiver buffers
TCP
code
receiver protocol stack
from sender
recv()

## Slide 17: But socket buffers can get full…
Applications may read data slower than the sender is pushing data in
  Example: what if an app infrequently or never calls recv()?
There may be too much reordering or packet loss in the network
  What if the first few bytes of a window are lost or delayed?
Receivers can only buffer so much before dropping subsequent data
application
process
TCP socket
receiver buffers
TCP
code
receiver protocol stack
from sender

## Slide 18: Goal: avoid drops due to buffer fill
Have a TCP sender only send as much as the free buffer space available at the receiver.
Amount of free buffer varies over time
TCP implements flow control
Receiver’s ACK contains the amount of data the sender can transmit without running out the receiver’s socket buffer
This number is called the advertised window size
application
process
TCP socket
receiver buffers
TCP
code
receiver protocol stack
from sender

## Slide 19: Flow control in TCP headers

## Slide 20: TCP flow control
Receiver advertises to sender (in the ACK) how much free buffer is available
Sender
Receiver
1
2
3
4
1
2
4
5
3

## Slide 21: TCP flow control
Subsequently, the sender’s sliding window cannot be larger than this value
Restriction on new sequence numbers that can be transmitted
Restriction on TCP sending rate
Sender
Receiver
1
2
3
4
1
2
4
5
3
0
1
2
3
4
5
6
7
1
0
Last cumulative
ACK’ed seq #
Last transmitted
seq #
Window <= Advertised window
Sender’s view:

## Slide 22: TCP flow control
If receiver app is too slow reading data:
  receiver socket buffer fills up
  So, advertised window shrinks
  So, sender’s window shrinks
  So, sender’s sending rate reduces
Sender
Receiver
1
2
3
4
1
2
4
5
3
0
1
2
3
4
5
6
7
1
0
Last cumulative
ACK’ed seq #
Last transmitted
seq #
Window <= Advertised window
Sender’s view:

## Slide 23: TCP flow control
Flow control matches the sender’s write speed to the receiver’s read speed.
Sender
Receiver
1
2
3
4
1
2
4
5
3
0
1
2
3
4
5
6
7
1
0
Last cumulative
ACK’ed seq #
Last transmitted
seq #
Window <= Advertised window
Sender’s view:

## Slide 24: Sizing the receiver’s socket buffer
Operating systems have a default receiver socket buffer size
  Listed among the parameters in sysctl –a | grep net.inet.tcp on MAC, sysctl –a | grep net.ipv4.tcp on Linux
If socket buffer is too small, sender can’t keep too many packets in flight  lower throughput
If socket buffer is too large, too much memory consumed per socket
How big should the receiver socket buffer be?

## Slide 25: Sizing the receiver’s socket buffer
Case 1: Suppose the receiving app is reading data too slowly:
  no amount of receiver buffer can prevent low sender throughput if the connection is long-lived

## Slide 26: Sizing the receiver’s socket buffer
Case 2: Suppose the receiving app reads sufficiently fast on average to match the sender’s writing speed.
  Assume the sender has a window of size W.
  The receiver must use a buffer of size at least W. Why?
Captures two cases:
(1) When the first sequence #s in the window are dropped
  The rest of the window must be buffered until the ACKs (of the rest of the window) reach sender. Adv. window in ACKs reduces sender’s window
(2) When the sender sends a burst of data of size W
  Receiver may not match the instantaneous rate of the sender

## Slide 27: Summary of flow control
A mechanism to keep buffers available at the receiver whenever the sender transmits data
Main function: match sender speed to receiver speed
Socket buffer sizing is important for throughput